## Slide 1: BOLT Thunderstorm Tracking
Zen KAWASAKI
Professor Emeritus at Osaka University
RAIRAN Pte. Ltd.

## Slide 2
Lightning triggered by an airplane (movie)

## Slide 3
Lightning triggered by an airplane (frame by frame)
１.
２.
３.
４.
５.
６.
７.
８.
９.
An evidence of a bi-directional leader initiation

## Slide 4: BOLT deployment diagram
Internet or Mobile
(Per site)
Server
Analyzer
Display
Internet Distribution
This layout can be applicable for any ‘N’ Sites.
(‘N’ = No. of sites)
Main Stations
Local Stations
LF Antenna
Including Amp.
GPS
BOLT remote station
Site 1
LF Antenna
Including Amp.
GPS
BOLT remote station
Site N

## Slide 20
Real time 3D monitoring is possible.
Height as a function of time
Height VS East-west cross section
Projection on the ground
Height VS North-
south cross section

## Slide 21
An example of BOLT 3D observation
The top panel is the altitude of BOLT location as a function of time.
The second panel is the west to east cross section. The ordinate is the height.
The bottom right panel is the north to south cross section, and abscissa is the height of BOLT location
The bottom left is the BOLT location projected on the
A color time code is applied, cool color to warm one

## Slide 23: BOLT existing configuration and specifications in Osaka, Japan
Specifications | 
Pass band | ～500kHz
Sampling rate | 4MHz
Amplitude Resolution | 16 bit
Time resolution | 1 ms
Time constant | 200 μs
20 km
Antenna array
50km
BOLT antenna
Antenna sites

## Slide 24
BOLT antenna
BOLT local station
Easy installation! Both are able to be deployed on the ground and on the roof.

## Slide 25
Total power consumption: 50Watts
Operating voltage: 100volts -240volts
Preferable temperature range: -20 to +50 degrees
Ventilation is equipped with 2 watts fan.
Water proof is guaranteed.
BOLT improved looks for Local Control Box

## Slide 26
Classical VLF/LF(Existing System)
Radiation from strokes
  One LF pulse per stroke
  Low spatial and time resolution
  Like still picture
  Our VLF/LF BOLT
Radiation from discharge development
  One thousand pulses for LF
  High spatial and time resolution
  Like movie picture
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
× One thousand locations/1flash
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
One location/1stroke
Electromagnetic wave remote sensing

## Slide 27
BOLT locations overlay on the RADAR echo (CAPPI).
Squares are the positions of BOLT location.
Radiuses are 20km, 40km and 60km respectively.
A red dot is the position where we expect the warning.
The cloud system travels from west to east.
Warning : when clouds edge crosses to 20km!!
We can issue a warning in 20 minutes in advance to evacuate. It is believed to be sufficient.
This is an evidence of prediction by BOLT.
Warning at 5:37, and lightning strikes at 5:57.

## Slide 28
BOLT configuration in Singapore and location accuracy
Seven BOLT antennas are sufficient to cover whole Singapore.

## Slide 29: Principle and feature of BOLT
LF electromagnetic pulse associated with electrical activity
Maximum one thousand location for one second in real time
In case of optional function, 3D is given by thousands location
A passive RADAR with higher time resolution than conventional one
Total electrical activity in severe storms is imaged.
Heavy precipitation and lightning strike can be forecasted in 10 minutes advance.

## Slide 30: The tentative goal of RAIRAN
Solution Business for Natural Disaster Prevention
  Sales activity for remote sensing technology and information
  Monitor center in Singapore of rain, thunderstorm and Tsunami
  Collaboration with Weather Matrix Pte. Ltd.
Technical transfer of innovation to the South-East Asia
  Technical transfer to support ASEAN country
  Education and digging out possible solution business
  Further understanding of Global warming through observations

## Slide 31
BOLT observations are equivalent to thunderstorm observations from the aspect of precipitations.
The final goal is the BOLT operation whole over South-East Asia

## Slide 32
GOAL:
Operation of BOLT
over the South East Asia
Start from some local and
expand the coverage gradually!